## Slide 1
Indian Institute of Information Technology, Pune
Department of Electronics & Communication Engineering
Optimal Joint ISAC
Waveform Design for 6G Networks
Integrated Sensing & Communication · OFDM-MIMO · mmWave 28 GHz · 6G Networks
Prepared By:
Sandhya Samrath
Programme:
B.Tech – Electronics & Communication Engineering
Project Guide:
Prof. ___________________________
Academic Year:
2024 – 2025
OFDM
MIMO
CA-CFAR
QPSK
Pareto
CRB
mmWave
Rayleigh
Final Year Major Project Defense | B.Tech ECE | IIIT Pune | 2024–25

## Slide 2
INTRODUCTION
Introduction & Problem Statement
Why ISAC is critical for 6G — and what this project solves
What is ISAC?
Integrated Sensing And Communication — a unified system where a single waveform simultaneously performs radar sensing and wireless communication using shared spectrum, hardware, and signal processing.
Why Critical for 6G?
Spectrum scarcity demands dual-function waveforms
6G targets sub-ms latency + sensing fusion for V2X, drones, smart cities
28 GHz mmWave offers 100 MHz+ bandwidth for both functions
Separate System Waste
Traditional systems deploy dedicated hardware for radar + comms separately — doubling spectrum usage, cost, and size.
Spectrum Congestion
6G mmWave bands are limited. Sharing a single OFDM waveform between sensing pilots and data subcarriers is essential.
No Balanced Design
Existing work optimises either sensing OR communication. A joint Pareto framework for balanced ISAC design is lacking.
This project: Design a joint OFDM-ISAC waveform for 28 GHz 6G using shared pilot/data subcarriers, MIMO beamforming, and Pareto-optimised sensing-communication balance.

## Slide 3
OBJECTIVES
Project Objectives & Literature Review
Three design approaches considered — Joint Design selected
Project Objectives
1
Design joint OFDM waveform for 28 GHz 6G with shared pilot (sensing) and data (comm) subcarriers
2
Implement 8×4 MIMO beamforming for spatial gain in both sensing and communication directions
3
Achieve accurate radar ranging via Range-Doppler processing + CA-CFAR detection
4
Evaluate communication performance: BER, EVM, SE under Rayleigh fading with MMSE equalisation
5
Derive CRB bounds for range/velocity estimation and compare with simulated RMSE
6
Optimise α (pilot ratio) and β (power split) via Pareto surface to find practical knee-point
Approach A
Sensing-Centric
Comm link treated as secondary. Maximises radar SINR and range resolution. Limitation: poor BER, unsuitable for 6G data services.
Approach B
Communication-Centric
Radar sensing treated as secondary. Good BER but degrades sensing: high RMSE, missed detections. Not viable for dual-function 6G.
Approach C
Joint Design ✓ Selected
Jointly optimises α and β via Pareto framework. Balances sensing and comm — knee-point at α≈0.40 gives best practical tradeoff.
Key Literature Gaps Addressed:
No prior work combines dynamic α/β optimisation + percentile CFAR + Pareto knee-point analysis in a single end-to-end 28 GHz OFDM-ISAC simulation framework.

## Slide 4
ARCHITECTURE
Complete System Architecture
End-to-end OFDM-ISAC pipeline: S1 → S8
S1
System
Parameters
fc=28GHz
BW=100MHz
256 SC · 128 sym
S2
MIMO
Beamforming
8×4 MIMO
Array steering
Beam weights
S3
OFDM-ISAC
Transmitter
Pilot: Sensing
Data: Comm
QPSK · IFFT+CP
S4
Dual-Path
Channel
Radar: echo
Comm: Rayleigh
AWGN noise
S8
Pareto
Optimisation
U(α,λ) surface
Knee α≈0.40
Global optimum
S7
CRB &
Detection
Fisher Info
Swerling models
Pd vs SNR
S6
Comm
Receiver
LS Estimation
MMSE Equalise
BER · EVM · SE
S5
Radar
Receiver
Range-Doppler
CA-CFAR
SINR · RMSE
Shared Waveform · Joint α/β Optimisation · Dual-Path Channel · MATLAB End-to-End Simulation

## Slide 5
METHODOLOGY
Proposed Methodology
S1–S8 module design with key equations and parameters
S1
System Parameters
fc=28GHz · BW=100MHz · Nsc=256 · Nsym=128 · Ncp=32
S2
MIMO Beamforming
w = a(θ)/‖a(θ)‖ · Array: 8Tx × 4Rx · d = λ/2
S3
OFDM-ISAC Transmitter
s[n] = IFFT{X} · α=pilot ratio · β=power split · QPSK
S4
Dual-Path Channel
H_radar: freq-domain echo · H_comm: Rayleigh + AWGN
S5
Radar Receiver
R-D Map: IFFT×FFT · CFAR: percentile threshold · SINR, RMSE
S6
Communication Receiver
Ĥ = Y_p/X_p (LS) · MMSE EQ · BER, EVM, SE
S7
CRB + Detection Prob.
J(τ) = 8π²BW²·SNR/c² · Pd vs SNR · Swerling 0/I/III
S8
Pareto Optimisation
U(α,λ) = α·Qsense + (1-α)·λ·SE · Knee: α*≈0.40
Final Operating Point: α = 0.40 | β = 0.75 | SNR = 20 dB | M = 4 (QPSK) | Nt = 8 | Nr = 4 | fc = 28 GHz
Pareto Knee Point | CRB Range = 0.411 m | CRB Velocity = 0.626 m/s | MATLAB Simulation

## Slide 6
IMPLEMENTATION
Core Implementation
MIMO Beamforming · OFDM-ISAC Transmitter · Dual-Path Channel
MIMO Beamforming
Configuration:
8 Tx × 4 Rx antennas, d = λ/2
Steering Vector:
a(θ) = [1, e^{j2πdsinθ/λ}, …]
Beam Weight:
w = a(θ) / ‖a(θ)‖
ISAC Beams:
3 target directions + comm beam
Gain Result:
−1.4 / +2.3 / +1.4 dB (targets)
OFDM-ISAC Transmitter
Subcarrier Allocation (Nsc = 200 active):
Pilot (40%)
Sensing
Data (60%) Comm
Modulation:
QPSK (M=4), 2 bits/symbol
Pilot Power:
Ppilot = Psense / Npilot_sc
Data Power:
Pdata = Pcomm / Ndata_sc
Waveform:
s[n] = IFFT{X} + CP (Ncp=32)
Beamformed:
S_tx = w · s[n]
Dual-Path Channel
Radar Path:
Freq-domain echo: H_r[k,l] = Σ σ·e^{-j2πkΔf·τ}
Comm Path:
Rayleigh flat fading: h ~ CN(0,1)
Noise:
AWGN: σ² = P_total/SNR_lin
CP Guard:
Ncp=32 samples covers echoes up to 320 m
SNR:
Operating at 20 dB (SNR_lin = 100)
Key Design Parameters
α = 0.40 (pilot fraction) | β = 0.75 (power to comm) | Pcomm = 0.75 W | Psense = 0.25 W | Ptotal = 1.0 W (normalised)

## Slide 7
RECEIVER DESIGN
Receiver Design
Radar: Range-Doppler + CA-CFAR · Comm: LS + MMSE + BER/EVM
Radar Receiver (S5)
Step 1
Pilot extraction: H[k,l] = Y_pilot / S_tx_pilot
Step 2
Hann window (range+Doppler), IFFT → range resp.
Step 3
FFT (Doppler) → 2D Range-Doppler map
Step 4
Range profile: max power across Doppler bins
Step 5
CA-CFAR: 40th-percentile noise est. + cluster merge
Result
3 detections · SINR=23.12dB · RMSE=1.479m
T[i] = κ · prctile(training_cells, 40) — replaces mean → eliminates sidelobe inflation
Communication Receiver (S6)
Step 1
Remove CP → FFT → extract data+pilot subcarriers
Step 2
LS Channel Est: Ĥ = Y_pilot / X_pilot
Step 3
MMSE EQ: Ŷ = Y · conj(H) / (|H|² + σ²)
Step 4
QPSK demod → bit stream → BER computation
Step 5
EVM: ‖Ŝ−S‖ / ‖S‖ × 100%
Result
BER=7.18×10⁻² EVM=90.3% SE=3.75bps/Hz
SE = Σ log₂(1 + |H[k]|² · Pdata / σ²) per data subcarrier → 3.75 bps/Hz at α=0.40, β=0.75

## Slide 8
OPTIMISATION
Optimisation & Mathematical Results
CRB Analysis · Detection Probability · Pareto Surface · Knee Point
CRB Analysis (S7)
CRB Range:
J(τ) = 8π²·B_eff²·SNR / c²
→ CRB_R = 0.411 m
CRB Velocity:
J(v) = 8π²·f_c²·T_CPI²·SNR / c²
→ CRB_V = 0.626 m/s
RMSE vs CRB:
Simulated RMSE = 1.479 m
Approaches CRB bound
Significance:
Confirms radar chain operates near theoretical optimum
Detection Probability (S7)
Chart: 
| -5 | 0 | 5 | 10 | 15 | 20 | 25
Swerling 0 | 0.05 | 0.12 | 0.35 | 0.72 | 0.92 | 0.97 | 0.99
Swerling I | 0.02 | 0.07 | 0.2 | 0.52 | 0.82 | 0.95 | 0.98
Swerling III | 0.01 | 0.04 | 0.12 | 0.38 | 0.7 | 0.9 | 0.96
SNR (dB)
Pareto Optimisation (S8)
Chart: 
| 0.05 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Utility U(α) | 0.88 | 0.84 | 0.77 | 0.7 | 0.61 | 0.52 | 0.4 | 0.28 | 0.15
Utility Function:
U = α·Qsense + (1-α)·λ·SE
Global Optimum:
α*=0.05, λ*=1.00 (comm-heavy)
Knee Point ★:
α≈0.40 — balanced ISAC choice
Mathematical Basis: CRB sets theoretical bound · Swerling models realistic target fluctuation · Pareto utility identifies optimal operating region

## Slide 9
RESULTS
Final Simulation Results & Comparison
Operating Point: α=0.40 · β=0.75 · SNR=20dB · 28GHz · 8×4 MIMO
23.12 dB
Radar SINR
1.479 m
Range RMSE
3 / 3
CFAR Detections
7.18×10⁻²
BER (QPSK)
3.75 bps/Hz
Spectral Efficiency
90.3%
EVM
Detected Target Ranges: T1 = 82 m · T2 = 149 m · T3 = 278 m (True: 80, 150, 280 m) · Max error < 3 m
Performance Metric | Sensing-Only System | Comm-Only System | This Work (ISAC)
Radar SINR | ~25 dB | N/A | 23.12 dB ✓
Range RMSE | ~1.2 m | N/A | 1.479 m ✓
BER | ~0.45 (poor) | ~0.01 (ideal) | 7.18e-2 ✓
SE (bps/Hz) | ~1.2 | ~5.8 | 3.75 ✓
CFAR Detections | ~5–6 (FAs) | N/A | 3/3 exact ✓

## Slide 10
CONCLUSION
Conclusion & Future Scope
Summary · Advantages · Limitations · Next Steps
23.12 dB
Radar SINR
1.479 m
Range RMSE
3 / 3
CFAR Det.
7.18×10⁻²
BER
3.75
SE bps/Hz
Key Conclusions
Unified OFDM waveform successfully performs both radar sensing and wireless communication at 28 GHz
CA-CFAR with percentile thresholding achieved exact 3/3 target detection, eliminating false alarms
BER improved 7× from initial 0.50 to 7.18×10⁻² via QPSK + normalised MMSE equalisation
Pareto knee-point at α=0.40 provides the best practical sensing-communication balance
End-to-end simulation validated CRB bounds, detection curves, and Pareto trade-off surface
Advantages
Single hardware for dual function — reduces cost and size for 6G base stations
Dynamic α/β tuning allows real-time adaptation to sensing vs. comm priority
Percentile-CFAR robust against sidelobe contamination in dense target environments
Pareto knee-point design criterion is practical and mathematically justified
Limitations & Future Scope
BER (7.18×10⁻²) still above ideal AWGN — needs pilot-aided adaptive channel tracking
Extend to multi-user ISAC with simultaneous sensing of multiple communication UEs
Implement machine learning-based adaptive CFAR thresholding for varying clutter
Hardware-in-loop validation on USRP/SDR testbed at 28 GHz mmWave
Explore IRS-assisted ISAC to extend sensing range and communication coverage
Thank You for Your Attention · Open for Questions · Sandhya Samrath · B.Tech ECE · IIIT Pune · 2024–25